## Slide 1: Implications of a changing climate for flood risk
Dennis P. Lettenmaier
Department of Geography
University of California, Los Angeles
Climate Roundtable, “Precipitation in the U.S.”
FM Global, Boston
Jan 12, 2015

## Slide 2: Motivating question: As the climate (and presumably precipitation and precipitation extremes) change, what will happen (is happening) to flood risk?

## Slide 3: Outline of this talk
What causes a flood?
Evidence for changes in U.S. flood risk
Sensitivities and projections
How good are the models?

## Slide 4: What causes a flood?
Extreme precipitation
Precipitation duration relative to catchment response time (“time of concentration”)
Soils, topography, and (lesser extent) vegetation
Catchment and storm geography; storm movement relative to catchment geography
Antecedent conditions (soil moisture)
Other factors (e.g., snow; frozen ground)

## Slide 5
precipitation
hydrological processes
channel processes
DOMINANT PROCESS
CATCHMENT SIZE
small
medium
large
flash flood
large river flooding
Dominant processes governing catchment storm response

## Slide 6
Pecos River flood frequency distribution (from Kochel et al, 1988)
Issues in the historical record

## Slide 7: Evidence for changes in U.S. flood risk

## Slide 8
A warmer climate, with its increased climate variability, will increase the risk of both floods and droughts
IPCC WG2, 2007

## Slide 9: Most climate scientists agree that global warming will result in an intensification, acceleration or enhancement of the global hydrologic cycle, and there is some observational evidence that this is already happening.
UNESCO World Water Development Report Water in a Changing Climate, 2009

## Slide 10
Total U.S. flood damages, 1934-2000
from Pielke et al., 2000

## Slide 11: First, (extreme) precipitation trends

## Slide 12: Extreme precipitation should be increasing as the climate warms

## Slide 13
replotted from Westra et al., J Clim, 2013
Relationship between annual daily maximum precipitation distribution and global mean temperature (red significantly positive, blue significantly negative, other no relationship)

## Slide 14
Trends in annual precipitation maxima in 100 largest U.S. urban areas, 1950-2009
from Mishra and Lettenmaier, GRL 2011

## Slide 22: So what about flooding?

## Slide 23
Number of statistically significant increasing and decreasing trends in U.S. streamflow (of 395 stations) by quantile (from Lins and Slack, 1999)

## Slide 24
About 10% of the 400 sites show an increase in annual maximum flow from 1941-71 to 1971-99
Maximum flow
Increase
No change
Decrease
Visual courtesy Bob Hirsch, figure from McCabe & Wolock, GRL, 2002
Notes: Location of sites with significant (based on t-change) change in annual maximum flow.

## Slide 25
Decadal Magnification Factors of Floods – Sites w/ no regulation
1,642 of 14,893 USGS Gage Sites with M>1 and p>0.9
From Yaindl and Vogel, 2009
visual courtesy Rich Vogel

## Slide 26
Decadal Flood Magnification Factors - HCDN Sites
208 of 1,588 HCDN Gage Sites with M>1 and p>0.9
From Yaindl and Vogel, 2011
visual courtesy Rich Vogel

## Slide 27
Decadal Flood Magnification Factors
Sites With No Regulation
From Yaindl and Vogel, 2011
visual courtesy Rich Vogel

## Slide 28
Results
Decadal Flood Magnification Factors
From Yaindl and Vogel, 2011
3 Groups of USGS Gages
visual courtesy Rich Vogel

## Slide 29: Paradox: Given increases in precipitation and runoff, why are there so few significant trends in floods?
Visual courtesy Tim Cohn, USGS

## Slide 30: Possible explanation
[Lins and Cohn, 2002]
Visual courtesy Tim Cohn, USGS
Notes: From USGS regional regression equations

## Slide 31: Sensitivities and projections

## Slide 32
Predicting urban flooding in a future climate – Thornton Creek example

## Slide 33
Global Climate Models
ECHAM5 • Developed at Max Planck Institute for Meteorology (Hamburg, Germany) • Used to simulate the A1B scenario in our study CCSM3 • Developed at National Center for Atmospheric Research (NCAR; Boulder, Colorado) • Used to simulate the A2 scenario in our study

## Slide 34
Global Climate Models
Mote et al 2005
ECHAM5
CCSM3
Notes: Note: A2 scenarios are solid, B1 scenarios are dashed

## Slide 35
Dynamical Downscaling
Courtesy Eric Salathé
Global Model
Regional Model

## Slide 36
Results of Future Analysis
 | SeaTac | Spokane | Portland
1-hour | +16% | +10% | +11%
24-hour | +19% | +4% | +5%
1-hour | -5% | -7% | +2%
24-hour | +15% | +22% | +2%
* Statistically significant for difference in means and distributions, and non-zero temporal trends
ECHAM5/WRF
CCSM3/WRF
*
*
*
*
Changes in average annual maximum precipitation between 1970–2000 and 2020–2050:

## Slide 37
Results of Bias Correction -- SeaTac
 | Raw Change | Corrected Change
1-hour | +16% | +14%
24-hour | +19% | +28%
1-hour | -5% | -6%
24-hour | +15% | +14%
ECHAM5
CCSM3
Comparison of changes in average annual maximum between 1970–2000 and 2020–2050:
*
* Statistically significant for difference in means and distributions, and non-zero temporal trends
*
*
*

## Slide 38
Thornton Creek

## Slide 39
Results of Hydrologic Modeling
Changes in average annual maxima streamflow at outlet of watershed between 1970-2000 and 2020-2050:
 | Juanita Creek | Thornton Creek
CCSM3 | +25% | +55%
ECHAM5 | +11% | +28%
* Statistically significant for difference in means
*
*

## Slide 43
Hydrological modeling (forced at the land surface with P, T, …)

## Slide 46: Simulation Approach
  10 GCMs from CMIP5: CCSM4, NorESM-1, bcc-csm1-1-m, CanESM2, HadGEM2-CC365, HadGEM2-ES365, MIROC5, IPSL-CM5A-MR, CSIRO-Mk3-6-0,CNRM-CM5
  3 Scenarios: Historical (1950-2005), RCP4.5 (2006-2100) and RCP8.5 (2006-2100)
Variable Infiltration Capacity Model
Multi-Model Ensemble Average
P and T
MACA Downscaling Method (to 1/16 deg spatial resolution)
P and T
Runoff, SWE
Notes: Here we use a subset of ten of the IPCC 5th Assessment Report (AR5) global climate models as archived by the Coupled Model Intercomparison Project 5 (CMIP5). These were chosen by comparing precipitation and temperature data from the gcms to 20th century observations and determining “best performers” due to a number of metrics, including diurnal variation, amplitude of seasonal cycle. for more on this, see Rupp et al 2013)
MACA downscaling: (see Abatzoglou and Brown 2011) is a statistical downscaling method that utilizes a meteorological observation dataset as training data to eliminate historical biases and to match spatial patterns in climate model output.
Downscaled from native resolution of GCMs (which varies across GCMs) to 4 or 6 km.
Scenarios: 1950-2005 for historical, 2006-2100 for RCP4.5 and 8.5. Representative concentration pathways correspond to different levels of radiative forcing due to greenhouse gas emissions, relative to pre-industrial levels. 4.5 is a ‘business as usual’ scenario, where emissions peak around 2040 and then decline. in 8.5, emissions continue to rise throughout the 21st century.
VIC model: macroscale, semi-distributed land surface hydrologic model
For this study, we are concerned with how RCP4.5 and 8.5 will impact flood frequency across the Pacific Northwest region of the United States.

## Slide 47: Assessment of potential flood changes in PNW based on (10) CMIP5 scenarios

## Slide 48: Future Changes in the Mean Annual Maximum Flood
Notes: For this analysis, we take the annual maximum 24-hr runoff for each year of the period, 1950 to 2005 for historical, 2006-2100 for rcp 4.5 and 8.5, and take the mean of the maxima over the time period. The left plot is the ratio of the mean for 4.5 to historical, and the right side is the ratio of the mean for 8.5 to historical. Here the ratio ranges from 0.5 to 1.5, which corresponds to a range between 50% reduction to 50% increase in the amount of the maximum annual flood.
What we can take from this is that there is an increase in the intensity of the annual maximum flood in almost every part of the Pacific Northwest, excluding Central Idaho, and there is a marked increase in the annual maximum flood between 4.5 and 8.5 scenarios.
We also want to know how the timing of the mean annual maximum flood is changing.

## Slide 49: Timing of Annual Maximum Flood
Notes: The top row shows the timing of the annual maximum flood by showing the Julian day of the year of the flood. The leftmost plot is for the historical period, and the center and rightmost plot show the Julian day for 4.5 and 8.5 respectively.
The bottom row shows the change in the Julian day for 4.5 and 8.5, with white showing no change. We see that the annual maximum flood is moving earlier in the year in almost all cases, and this is particularly strong in the Snake Region and parts of the Northern Rockies, with a shift of 2-3 weeks in many parts of the basin, with a further increase for rcp8.5.
Given these changes in the intensity and timing of the annual maximum flood, we want to ask FLIP TO NEXT SLIDE

## Slide 50
Are these changes driven by SWE, Precipitation, or Temperature?

## Slide 51: Future Changes in Mean Annual 24-hr Maximum Precipitation
Notes: Here we run the same analysis as with the mean annual maximum flood, taking the annual maximum 24-hr precipitation for each year of the historical and future periods and the mean over the yearly maxima. the leftmost plot shows the magnitude of the historical annual maximum, and the center and right plots show the ratio of the mean annual maximum precipitation during for the future rcp4.5 scenario to historical and future rcp8.5 scenario to historical, respectively.
We see that there is a very strong increase in the intensity of annual maximum precipitation for the majority of the Pacific Northwest, excluding the Canadian portion of the Pacific Northwest and the Oregon coast. There is a strong increase between 4.5 and 8.5 as well.

## Slide 52: Ratio of April 1 SWE to Cumulative NDJFM Precipitation
0-0.1: Rain Dominant
0.2-0.4: Transient
0.5-1: Snow-Dominant
(see Elsner et al 2010)
Notes: Based on the warming and precipitation trends discussed earlier, we want to understand how they will drive the hydrology of the Pacific Northwest. Here we use an index that was used in the Elsner et al 2010 paper: we take the ratio of aggregate April 1 Snow water equivalent to cumulative winter precipitation to classify basins as rain dominant, transient, or snow dominant. Ratios of 0-0.1 represent rain dominant basins, 0.2-0.4 are transient, and 0.5-1 are snow-dominant, to varying degrees.
Studies have shown that climate change will push transient basins toward being rain dominant. We see this effect in our simulations, with a more and more transient basins in the interior and the Snake Region becoming rain dominant. We also see watersheds in the Northern Rockies becoming less and less snow dominant between the historical to rcp8.5 scenarios.

## Slide 53
Notes: When we look at temperature, we see a stronger increase in warming for summer than winter temperature. Here the leftmost column of plots is the historical winter and summer temperature magnitudes, the center represents the degree change in Celsius between the rcp4.5 future scenario and the historical period, and the rightmost column shows the degree change in Celsius between rcp8.5 and the historical period.
We see that that the winter temperature change for future scenarios goes from around 2-3 degrees for rcp4.5 to 3-4.5 for rcp8.5. For summer temperature, we see an increase of 2-4 degrees for rcp4.5 and then an increase of 3 to almost 6 degrees for rcp8.5.
So the temperature increases are significantly stronger for rcp8.5, and particularly so for summer temperature.

## Slide 54: Future Changes in April 1 SWE
Notes: With the classification results from the previous slide, it helps to look at historical versus future April 1 SWE magnitudes. The top row here is of the mean April 1 snow water equivalent for the historical 1950-2005 period, and the center and right plots in the top row are of rcp4.5 and 8.5 magnitudes for 2006 to 2100. We see a progression with more and more watersheds falling below 75 mm of SWE.
But in the bottom row, which represents the ratio of rcp4.5 mean April 1 SWE to historical SWE, and rcp8.5 mean April 1 SWE to historical, we see a stronger trend of decreasing SWE. Nowhere in the Pacific Northwest is there more than about 0.8% of historical levels, and in some parts of the region, there is 25-50% of historical levels. There is a particularly strong difference between the two scenarios along the WA/OR coast and in the Canadian portion of the Northern Rockies.

## Slide 55: Summary of Results
Changes in timing primarily driven by warming
    summer warming stronger than winter warming, with significant differences between rcp4.5 and 8.5
    on average, floods will come earlier by 2 - 3 weeks
Changes in flood frequency primarily driven increases in intense precipitation
Next Steps: investigate duration of maximum flood event, expand analysis to regional level
Notes: except at highest elevations and coldest basins, such as the upper elevations of the Cascades and parts of the Northern Rockies, wintertime p will shift toward rain resulting in thinner April 1 SWE and earlier occurrence of max annual flood
changes in flood frequency perhaps due to atmospheric river events, at least in the Cascades
investigating the duration of the flood event that produces the annual maximum flood
calculating extreme flow statistics
expand analysis from local, i.e. HUC-08 level, to regional level to account for inflows from upstream areas

## Slide 56: How good are the models?

## Slide 58: The appropriate test of downscaling’s relevance is not whether it alters paradigms of global climate science, but whether it improves understanding of climate change in the region where it is applied.

## Slide 59
The November Surprise
JAN
FEB
MAR
APR
MAY
JUN
JUL
AUG
SEP
OCT
NOV
DEC
Courtesy Eric Salathé
NOV

## Slide 60
Can RCMs reproduce the timing of precipitation maxima ?
Winter
Summer
from Mishra et al., GRL 2012

## Slide 61: Summary
“Preponderance of evidence” for (some) increase in precipitation extremes
Not showing up in flood records (why not?)
Flooding in western U.S. is sensitive to warming (in observations) aside from changes in precipitation extremes
Climate signal (in flooding) is most likely being obscured by lots of natural variability
Opportunities (for enterprising graduate students) to better understand the interaction of climate (change) and flood risk across the U.S.